By the numbers

| Height: | 630 feet (192 meters) |
| --- | --- |
| Width: | 630 feet (192 meters) |
| Weight: | 17,246 tons |
| Height compared to a building (allowing 10 feet for every story): | 63 stories |
| Number of steps to the top (in each leg): | 1,076 |
| Number of landings in each stairway: | 105 |
| Size of observation room: | 7 ft. 2 in. wide, 65 ft. long, 6 ft. 9 in. tall (2.18m x 19.8m x 2.06m) |
| Maximum capacity of observation deck: | 140 persons |
| Number of windows in observation deck: | 32 |
| Dimension of windows: | about 7 in. x 27 in. (180mm x 690mm) |

| Number of tram cars: | 16 (8 in each leg) |
| --- | --- |
| Capacity of a tram car: | 5 people |
| Speed of trams: | 340 ft. per min. or 3.86 mph. |
| Maximum number of people who can ride to the top in 1 hour: | 240 on each tram |
| Approximate number of people who ride to the top each year: | Over 600,000 |
| Shape of Arch section: | equilateral triangle |
| Number of prefabricated sections assembled on site: | 142 |
| Width of largest sections, at base: | 54 ft. |
| Width of smallest section, at top: | 17 ft. |
| Thickness of stainless steel plates in outer skin: | 1/4" (6.3mm) |
| Amount of stainless steel in the Arch: | 900 tons |
| Shape of the Arch: | catenary curve, the shape a free-hanging chain takes when held at both ends |
| Amount of sway: | under normal conditions the Arch sways no more than ½”; it takes a 50-mile-per-hour wind to move it 1-1/2 in. off of center; under extreme conditions, the Arch is designed to sway as much as 9 in. off of center in either direction. |
| Required accuracy of measurement in construction: | within 1/64th of an inch |
| Number of lightening rods: | 7 |
| Degrees off true north-south orientation: | 18° |

| Milestone Dates |  |
| --- | --- |
| Park created: | December 1935 |
| First building cleared: | 1939 |
| Last building cleared | 1959 |
| Competition period: | 1947-1948 |
| Architect Eero Saarinan died: | 1961 |
| Construction began: | February 12, 1963 |
| Last piece installed at the top: | October 28, 1965 |
| Opened to the public: | north leg, July 1967; south leg, May 1968 |
| Visitor center opened: | June 1967 |
| First movie theater opened: | May 1972 |
| Museum opened: | August 1976 |
| 70mm movie theater opened: | March 1993 |
| Parking garage completed: | May 8, 1986 |
| People |  |
| First president of Jefferson National Expansion Memorial Association: | Luther Ely Smith |
| Architect: | Eero Saarinen |
| Engineers: | Fred Severud, Hannskarl Bandel |
| Landscape architect: | Dan Kiley |
| General contractor: | MacDonald Construction Company of St. Louis |

Operations

You may stay as long as you like (until closing time) in the observation deck at the top; average time of complete round trip to the top is 45 minutes

There is a tram to the top in each leg. If only one tram is operating on a given day, you must return on that tram. If both trams are operating, you may return on either side.

The tram ride takes four minutes to the top and three minutes to return to the ground. It takes about three minutes to unload and load passengers. Atram just leaving the top will return in approximately 10 minutes.

There are no facilities at the top of the Arch; there was never a snack bar or restaurant there.

A Park Ranger is always on duty at the top to assist people in boarding and unloading, to provide for safety, and to answer questions. Each Ranger works a single, two-hour shift at the top on a given day.

The 1,076 steps in the stairways of each leg are used by maintenance personnel only; visitors are not allowed to walk up or down.

To figure out how many people could go to the top in a year, consider this: during the summer season, each tram makes a maximum of 80 trips to the top; 40 tickets are sold for each trip, so 6,400 people can visit the top each day; during the winter season there are only 48 trips to the top each day on each tram.

The trams have been in operation since 1967 and carry nearly a million people a year to the top of the Arch.

Construction

The Arch is constructed with double-walled steel and concrete. There’s an outer wall (or skin) of ¼” stainless steel and an inner wall of 3/8” structural steel. At the bottom of the Arch, the distance between the inner and outer skins is 3 feet; at the top, it’s less than 1 foot. Up to about half its height, the space between the two skins is filled with concrete.

It cost $13,420,168 to construct the Arch. This included $1,977,750 for the internal tram system, paid by Bi-State Development Agency. The federal government paid three-quarters of the remaining cost, and the City of St. Louis paid one-quarter. Developing the Arch grounds cost under $5,300,373.

The last piece of the Arch to be installed was a triangle 17 feet long on each side and eight feet wide. It took over 500 tons of pressure to jack apart the almost-finished legs of the Arch to insert this last piece at the top.

Miscellaneous

The Mississippi River flows directly below the east windows of the Arch at a normal top water speed of 3 miles an hour at a depth of about 12-15 feet. The Missouri River meets the Mississippi about 15 miles to the north of the Arch.

The Arch has a series of lightning rods on the top which are grounded directly into bedrock, with a perfectly insulated interior. It is able to withstand hundreds of lightning bolts which hit it each year.

On a clear day the view at the top can extend up to thirty miles in either direction, however, St. Louis can be a very hazy city which reduces visibility at the top. On cool, damp mornings a dense fog can create zero visibility at the top.

# # #

# Text boxes

Jefferson National

Expansion Memorial

11 North 4th Street

St. Louis MO  63102

www.nps.gov/jeff

314-655-1600 phone

314-655-1641 fax

page 3

Immediate

Ann Honious

314  655-1634

7-1-2011

Press Release

page 2

Arch Fact Sheet

National Park Service

U.S. Department of the Interior

page 5

page 4

Release date:

Contact(s):

Phone number:

Date: