## Remote Automated Weather Station

Zion National Park has recently come on line with a second remote automated weather station (RAWS). This new RAWS is located in Zion Canyon (3900 ft.), near the Watchman residential area.  The other one is located at Lava Point (7950 ft.) and has been in operation since 1995.  These RAWS are two of 1500 such stations located throughout the United States (mainly in the west) that monitor weather data to assist land management agencies with a variety of projects – monitoring air quality, rating fire danger and providing information for research applications.

Most of the RAWS are owned by wildland fire agencies and are used to predict fire behavior and monitor fuels. They are placed in locations where wildland fires often occur. Each unit operates on 8-10 watts of power and has a battery that lasts approximately three years. RAWS units collect and store data every ten minutes and then transmit this data to a computer system at the National Interagency Fire Center (NIFC) in Boise, Idaho via the Geostationary Operational Environmental Satellite (GOES). The GOES is operated by the National Oceanic and Atmospheric Administration (NOAA).  On average, this data is transmitted every 60 minutes, but they can be programmed to transmit anywhere from 30 minutes to many hours. These data are automatically forwarded to several other computer systems including the Weather Information Management System (WIMS) and the Western Regional Climate Center in Reno, Nevada.

Weather is the most critical factor affecting fire behavior and therefore firefighter safety -- that's what makes RAWS units so important to fire managers. The weather station broadcasts weather observations and can be called over the radio by sending out a tone. If there are parameters that are critical to fireline safety, you can program that parameter for a variety of elements including wind shifts, humidity change, or sudden temperature rise or decline. If one of these parameters reaches a pre-determined critical level, RAWS will send out a tone to alert firefighters and thus increase the safety factor.

RAWS weather data for Zion National Park is accessible online via the following websites: www.wrh.noaa.gov/saltlake/fire/raws or www.boi.noaa.gov/firewx.htm Select either Zion Canyon or Lava Point for weather information at that particular location.

For more general information on RAWS visit www.fs.fed.us/raws.